## Slide 1: Eagle Stream Code Architecture Introduction
Insyde Software April 2021

## Slide 2: Copyright 2021 Insyde Software Corp., All Rights Reserved.
No part of this publication may be reproduced, transmitted, transcribed, stored in a retrieval system, or translated into any language or computer language, in any form, or by any means, electronic, mechanical, magnetic, optical, chemical, manual or otherwise, without the prior written permission of Insyde Software Corp.
Disclaimer
Insyde Software Corp. (“Insyde”), provides this document and the programs "as is" without warranty of any kind, either expressed or implied, including, but not limited to, the implied warranties of merchantability or fitness for a particular purpose.
This document may contain technical inaccuracies or typographical errors. Changes are periodically made to the information herein; these changes will be incorporated in future revisions of this document. Insyde is under no obligation to notify any person of the changes. Some code names featured in this document are used to identify products that are in development and not yet publicly announced for release. Insyde is not obligated for its accuracy or completeness.
This document may contain third party’s information, features, schedules, code names, and product names, which are based on Insyde’s interpretation available as of the creation of this document and may be changed from time to time. Neither Insyde nor the third party is obligated to notify such change. If you are interested in third party’s information, you may contact the local third party sales office or the local distributor to obtain the latest specifications. All the intellectual property right of any third party information remains to its owner or steward.

## Slide 3: Agenda
Goals & Target Audience
Introduce New Codebase Directory Structure (Insyde Kernel)
Eagle Stream Code Architecture
Introduce Multiple Workspaces
Override Mechanism
FSP
Compile
Internal Use

## Slide 4: Goal & Target Audience

## Slide 5: Goal & Target Audience
Target Audience:
    BIOS developers who use Eagle Stream to create their firmware products.
Goals:
    Be familiar with Eagle Stream code structure.
Requirements:
    Eagle Stream source code
    05.4x.yy.zzzz

## Slide 6: Introduce New Codebase Directory Structure (Insyde Kernel)

## Slide 7: Introduce New Codebase Directory Structure (1/3)
Support GIT source code control
GIT does NOT support to get code from 2 GIT repositories into 1 folder
  A directory named .git that contains all of necessary repository files for 1 GIT repository

## Slide 8: Introduce New Codebase Directory Structure (2/3)
New codebase directory structure prepare for coming GIT support
What does new codebase directory structure look like ?
  BaseTools : Build tool directory
  EDK2 : All EDK2 packages
  Insyde : Most InsydeXXX packages (Kernel code)
  Sio : SIO packages
  Intel(Amd)\chipset-name : Silicon related packages
  Oem : Feature and OEM feature packages
    Oem\feature-name : Feature packages
    Oem\oem-name : OEM packages
  Crb : Project board package
    Crb\Intel\chipset-crb-board
    Crb\Oem\feature-crb-board
    Crb\Oem\oem-crb-board
New Codebase Directory Structure

## Slide 9: Introduce New Codebase Directory Structure (3/3)
Optional packages are located under corresponding Feature directory
  EDK2\Feature
  Insyde\Feature
  Intel\chipset-name\Feature
  Oem\feature-name\Feature
  Oem\oem-name\Feature
Example : Console redirection package
  Insyde\Feature\InsydeCrPkg from InsydeCrPkg GIT repository

## Slide 10: Eagle Stream Code Structure

## Slide 11: InsydeH2O 5.x Code Structure Terminology
Reference Code Package – Vendor-maintained chipset support code.
Insyde Chipset Package – Insyde-maintained chipset support code.
Project Package – Insyde or OEM-maintained board support code.
Kernel Package – Insyde-maintained industry-standard or Insyde-standard support code.

## Slide 12: InydeH2O 5.4 Code Structure Folder Introduction
BaseTools: Base tool related binaries
Board: CRB or Project board package
EDK2: EDK2 modules
Insyde: Insyde kernel modules
Intel: Chipset related modules
SegFeature: SEG feature Packages
Sio: SIO related modules
Chipset
From Intel
Project
Insyde H2O Kernel

## Slide 13: InydeH2O 5.4 Code Structure Insyde Source Code Structure – Eagle Stream
ClientOenSiliconPkg: Eagle Stream usage limited to TraceHub, PCH PCIe Library at present
CpRcPkg: USRA, interface for silicon register accessing
CCMRC
EagleStreamChipsetPkg: Insyde Chipset support code
EagleStreamFspBinPkg: FSP related header files and binaries that are auto-generated during building.
EagleStreamFspPkg: Glue code to build Eagle Stream FSP Binary
ServerPlatformPkg: Sever common features
ServerRasPkg: Server RAS implementation (exclude some Memory RAS features)
ServerSecurityPkg: Server security implementation
ServerSiliconPkg: Silicon package

## Slide 14: InydeH2O 5.4 Code Structure Insyde Source Code Structure – SegFeature
InsydeAdvBootPkg: Codes for advanced boot options
InsydeEventLogPkg: Codes to handle BIOS logs
InsydeH2OUvePkg: Codes to support H2OUVE tool
InsydeIpmiPkg: IPMI modules & libraries
SegFeaturePkg: Assist other SEG feature packages

## Slide 15: Introduce Multiple Workspaces

## Slide 16: Introduce Multiple Workspaces (1/6)
EDK2 build tools allows to set multiple paths that will be searched when attempting to resolve the location of packages
  The new functionality is enabled through the addition of a new environment variable PACKAGES_PATH
PACKAGES_PATH environment variable is an ordered list of additional search paths
  The first path in the list has the highest priority and the last path has the lowest priority
  Paths using the default path separator of the host OS between each entry
    ‘;’ for Windows build environment and ‘:’ for Linux build environment
  The path specified by the WORKSPACE environment variable always has the highest search priority over any PACKAGE_PATH entries

## Slide 17: Introduce Multiple Workspaces (2/6)
PACKAGES_PATH is used for build tool to resolve the location of packages
Example 1: WORKSPACE=D:\Rev.5.4 PACKAGES_PATH=%WORKSPACE%\Insyde; %WORKSPACE%\EDK2
Q: In DSC or FDF file, “InsydeModulePkg/Universal/BdsDxe/BdsDxe.inf”. How build tool resolve the location ?
A: Build tools bases on following priority to find the file
  D:\Rev.5.4\InsydeModulePkg\Universal\BdsDxe\BdsDxe.inf --------------------[Not Found]
  D:\Rev.5.4\Insyde\InsydeModulePkg\Universal\BdsDxe\BdsDxe.inf ------------[Found]
  D:\Rev.5.4\EDK2\InsydeModulePkg\Universal\BdsDxe\BdsDxe.inf

## Slide 18: Introduce Multiple Workspaces (3/6)
Example 2: WORKSPACE=D:\Rev.5.4 PACKAGES_PATH=%WORKSPACE%\Insyde; %WORKSPACE%\EDK2
Q: MdeModulePkg/Core/Pei/PeiMain.inf { <SOURCE_OVERRIDE_PATH> MdeModulePkg/Override/Core/Pei } How build tool resolve the location ?
A: Build tools bases on following priority to find the file.
  D:\Rev.5.4\MdeModulePkg\Override\Core\Pei\PeiMain.c -------------------[Not Found]
  D:\Rev.5.4\Insyde\MdeModulePkg\Override\Core\Pei\PeiMain.c -----------[Not Found]
  D:\Rev.5.4\EDK2\MdeModulePkg\Override\Core\Pei\PeiMain.c ------------[Found]
  D:\Rev.5.4\MdeModulePkg\Core\Pei\PeiMain.c
  D:\Rev.5.4\Insyde\MdeModulePkg\Core\Pei\PeiMain.c
  D:\Rev.5.4\EDK2\MdeModulePkg\Core\Pei\PeiMain.c

## Slide 19: Introduce Multiple Workspaces (4/6)
Set the PACKAGES_PATH environment variable in ProjectSetup.bat

## Slide 20: Introduce Multiple Workspaces (5/6)
PROJECT_REL_PATH environment variable (Insyde specific)
  The directory, relative to WORKSPACE, of the directory that contains Project package
  Example : “D:\Rev.5.4\Board\Intel\EagleStreamMultiBoardPkg”
    WORKSPACE=D:\Rev.5.4
    PROJECT_PKG=EagleStreamMultiBoardPkg
    PROJECT_REL_PATH=Board\Intel
CHIPSET_REL_PATH environment variable (Insyde specific)
  The directory, relative to WORKSPACE, of the directory that contains chipset package
  Example : "D:\Rev.5.4\Intel\EagleStream\EagleStreamChipsetPkg "
    WORKSPACE=D:\Rev.5.4
    CHIPSET_PKG=EagleStreamChipsetPkg
    CHIPSET_REL_PATH=Intel\EagleStream
PROJECT_REL_PATH and CHIPSET_REL_PATH are used to correct the file path relative to the WORKSPACE for new directory structure in .bat, …, .cmd files

## Slide 21: Introduce Multiple Workspaces (6/6)
Make codebase support multiple workspaces
  PACKAGES_PATH used to correct build tool which attempts to resolve the location of packages
  PROJECT_REL_PATH and CHIPSET_REL_PATH used to correct the file path which relative to the WORKSPACE in .bat, …, .cmd files.
  PACKAGES_PATH, PROJECT_REL_PATH and CHIPSET_REL_PATH environment variables are set after setting WORKSPACE in ProjectSetup.bat
  PROJECT_REL_PATH and CHIPSET_REL_PATH value are obtained by GetProjectEnv.exe

## Slide 22: Override Mechanism

## Slide 23: How to Use Override Override in Project.dsc
Syntax
!disable Original_Path/Module.inf
Original_Path/Module.inf {
<SOURCE_OVERRIDE_PATH>
Override_Path}
Example
!disable MdeModulePkg/Universal/StatusCodeHandler/Smm/StatusCodeHandlerSmm.inf
MdeModulePkg/Universal/StatusCodeHandler/Smm/StatusCodeHandlerSmm.inf {
<SOURCE_OVERRIDE_PATH>
$(PROJECT_PKG)/Override/EDK2/MdeModulePkg/Universal/StatusCodeHandler/Smm }

## Slide 24: How to Use Override Example
The Override path use the New Codebase Directory Structure, so the path appended to $(PROJECT_PKG)/Override needs to use the relative path from WORKSPACE.
!disable MdeModulePkg/Universal/StatusCodeHandler/Smm/StatusCodeHandlerSmm.inf
MdeModulePkg/Universal/StatusCodeHandler/Smm/StatusCodeHandlerSmm.inf {
<SOURCE_OVERRIDE_PATH>
$(PROJECT_PKG)/Override/EDK2/MdeModulePkg/Universal/StatusCodeHandler/Smm
}
Support Multiple SOURCE_OVERRIDE_PATH
  The bottom of the override path has higher priority then upper in DSC <SOURCE_OVERRIDE_PATH> section.
  <SOURCE_OVERRIDE_PATH>
  OVERRIDE_PATH1 (Lowest priority)
  OVERRIDE_PATH2
  ...
  OVERRIDE_PATHN (Highest priority)

## Slide 25: FSP

## Slide 26: FSP (1/3)
The Intel Firmware Support Package provides the program for initializing Intel silicon and it needs to be integrated into a firmware environment to work.
FSP.bin
BIOS
Generate
Integrate
Intel FSP
source code

## Slide 27: FSP (2/3)
The Intel® FSP binary follows the UEFI Platform Initialization Firmware Volume Specification format.
Split into 3 separate FVs
  FSP-T: Temporary RAM initialization phase
  Primary purpose of this phase is to initialize the Temporary RAM.
  FSP-M: Memory initialization phase
  Primary purpose of this phase is to initialize the permanent memory
  FSP-S: Silicon initialization phase
  Primary purpose of this phase is to complete the silicon initialization
  including CPU and IO controller initialization.

## Slide 28: FSP (3/3)
FSP Binaries path: Intel\EagleStream\EagleStreamFspBinPkg
EagleStreamFspPkg.dsc and EagleStreamFspPkg.fdf describe the drivers and libraries that will be built and generated in FSP binaries
The PCD value used in the FSP binary file should be consistent with the project build

## Slide 29: Compile

## Slide 30: Compile
Eagle Stream supports the Native build and the FSP build.
Use the FSP build binary to test and tag BIOS.
The Native build binary will still do some simple tests.

## Slide 31: How to Compile Native
Generate the Binary
  Double click ProjectBuild.bat
    X64: Run “nmake uefi64” or “nmake efidebug”

## Slide 32: How to Compile FSP
Generate the Binary
  Double click ProjectBuild.bat
    X64:
      Run “BuildFsp.cmd /d” or “BuildFsp.cmd /r” to generate the FSP binary
      Run “nmake uefi64fsp” or “nmake efidebugfsp” to generate the full BIOS binary

## Slide 33: Thanks!

## Slide 34: Backup

## Slide 35: Support structure PCD