## Slide 1: SSID SVID Programming
Insyde Software March 2021

## Slide 2: Copyright 2021 Insyde Software Corp., All Rights Reserved.
No part of this publication may be reproduced, transmitted, transcribed, stored in a retrieval system, or translated into any language or computer language, in any form, or by any means, electronic, mechanical, magnetic, optical, chemical, manual or otherwise, without the prior written permission of Insyde Software Corp.
Disclaimer
Insyde Software Corp. (“Insyde”), provides this document and the programs "as is" without warranty of any kind, either expressed or implied, including, but not limited to, the implied warranties of merchantability or fitness for a particular purpose.
This document may contain technical inaccuracies or typographical errors. Changes are periodically made to the information herein; these changes will be incorporated in future revisions of this document. Insyde is under no obligation to notify any person of the changes. Some code names featured in this document are used to identify products that are in development and not yet publicly announced for release. Insyde is not obligated for its accuracy or completeness.
This document may contain third party’s information, features, schedules, code names, and product names, which are based on Insyde’s interpretation available as of the creation of this document and may be changed from time to time. Neither Insyde nor the third party is obligated to notify such change. If you are interested in third party’s information, you may contact the local third party sales office or the local distributor to obtain the latest specifications. All the intellectual property right of any third party information remains to its owner or steward.

## Slide 3: Agenda
Overview
Work Flow
Related Files
Customization Steps
Internal Use

## Slide 4: Overview

## Slide 5: Overview
Intel/EagleStream/$(CHIPSET_PKG)/CommonChipset/SetSsidSvidDxe/SetSsidSvidDxe.inf
  TIME: Program SSID/SVID at the PCI enumeration complete Event occurs
  DATA: Get SSID/SVID data from either PCD or default values
  HOW: Program a SSID/SVID value to a device
  WHOM: Program a SSID/SVID to specific devices

## Slide 6: Work Flow

## Slide 7: Work Flow
Start
Program on a specific devices
Program on a specific devices
Program on other devices
End
Program SSID/SVID on devices
if this device has not programmed
Program a SSID/SVID on a specific devices
if this device has not programmed
1) Program a SSID/SVID on a specific devices, which bus number > 0.
This handles by Insyde
2) Program a SSID/SVID on a specific add-in cards
This handles by customer.
No/Prog
No/Prog
Prog
Prog

## Slide 8: Related Files
Notes: SetSsidSvidDxe.c - DxeDriver

## Slide 9: Related Files - SetSsidSvidDxe
SetSsidSvidEntryPoint ()
  Program SSID/SVID at the PCI enumeration complete Event occurs
  The key content of SetSsidSvidDxe.c
SetSsidSvidDxe.c
EFI_STATUS
SetSsidSvidEntryPoint (
IN EFI_HANDLE ImageHandle,
IN EFI_SYSTEM_TABLE *SystemTable
)
{
...
Status = EfiCreateProtocolNotifyEvent (
  &gEfiPciEnumerationCompleteProtocolGuid,
TPL_NOTIFY,
SetSsidSvidCallBack,
NULL,
&Registration
);
...
}

## Slide 10: Related Files - SetSsidSvidDxe
SetSsidSvidCallBack ()
  Get SSID/SVID data from PcdDefaultSsidSvid or DeviceId+VendorId
SetSsidSvidDxe.c
VOID
EFIAPI
SetSsidSvidCallBack (
IN EFI_EVENT Event,
IN VOID *Context
)
{
...
SsidSvid = (UINT32)PcdGet32(PcdDefaultSsidSvid);
// Get the VID/DID as a default value
if (SsidSvid == 0) {
SsidSvid = ((UINT32)DeviceId << 16) + VendorId;
}
…
}

## Slide 11: Related Files - SetSsidSvidDxe
SetSsidSvidCallBack ()
  Program a SSID/SVID value to a device
SetSsidSvidDxe.c
VOID
EFIAPI
SetSsidSvidCallBack (
IN EFI_EVENT Event,
IN VOID *Context
)
{
...
// Program SSID/SVID...
Status = OemSvcUpdateSsidSvidInfo(Bus, Dev, Func, VendorId, DeviceId, ClassCode, SsidSvid );
if (!EFI_ERROR(Status)) {
continue;
}
Status = DxeCsSvcProgramChipsetSsid (Bus, Dev, Func, VendorId, DeviceId, SsidSvid);
if (!EFI_ERROR(Status)) {
continue;
}
ProgramSsidSvid (PciRootBridgeIo, Bus, Dev, Func, SsidSvid);
}

## Slide 12: Related Files - DxeOemSvcKernelLib
OemSvcUpdateSsidSvidInfo ()
  Program a SSID/SVID value to OEM specific device
OemSvcUpdateSsidSvidInfo.c
STATIC OEM_SSID_SVID_TABLE SsidTable[] = {
0x10DE, DEVICE_ID_DONT_CARE, ProgramSsidSvid0xFFFF10DE,
0x1002, DEVICE_ID_DONT_CARE, ProgramSsidSvid0xFFFF1002,
DEVICE_ID_DONT_CARE, DEVICE_ID_DONT_CARE, NULL
};
OemSvcUpdateSsidSvidInfo(
…
IN OUT UINT32 *SsidSvid
)
{
…
// Get special programming add-on device from OEM SsidTable.
for (Index = 0; SsidTable[Index].SpecialSsidSvidFunction != NULL; Index++ ) {
if (SsidTable[Index].VendorId == VendorId) {
if ((SsidTable[Index].DeviceId == DEVICE_ID_DONT_CARE) || (SsidTable[Index].DeviceId == DeviceId)){
Status = SsidTable[Index].SpecialSsidSvidFunction (Bus, Dev, Func, SsidSvid);
break;
}
}
}
…
}

## Slide 13: Related Files – DxeCsSvcProgramChipsetSSID.c
DxeCsSvcProgramChipsetSsid ()
  Program a SSID/SVID value to a device (For chipset-specific device)
  The key content of ChipsetSvcDxe.c
  DxeCsSvcProgramChipsetSSID.c
DxeCsSvcProgramChipsetSSID.c
EFI_STATUS
DxeCsSvcProgramChipsetSsid (
UINT8 Bus,
UINT8 Dev,
UINT8 Func,
UINT16 VendorId,
UINT16 DeviceId,
UINT32 SsidSvid
)
{
...
return mChipsetSvc->ProgramChipsetSsid (Bus, Dev, Func, VendorId, DeviceId, SsidSvid);
}

## Slide 14: Related Files – ProgramChipsetSSID.c
ProgramChipsetSsid ()
  Program a SSID/SVID value to a device (For chipset-specific devices)
  The key content of ProgramChipsetSsid.c
ProgramChipsetSsid.c
SPECIFIC_SSID_SVID_TABLE mSpecificSsidSvidTable[] ={
//{V_SA_IGD_VID , V_SA_IGD_DID , IgdSsidSvidSpecialProgramFunction},
{DEVICE_ID_DONT_CARE, DEVICE_ID_DONT_CARE, NULL}
};
ProgramChipsetSsid (
…
) {
for (Index = 0; mSpecificSsidSvidTable[Index].SpecialSsidSvidFunction != NULL; Index++ ) {
if (mSpecificSsidSvidTable[Index].VendorId == VendorId) {
if ((mSpecificSsidSvidTable[Index].DeviceId == DEVICE_ID_DONT_CARE)
|| (mSpecificSsidSvidTable[Index].DeviceId == DeviceId)){
mSpecificSsidSvidTable[Index].SpecialSsidSvidFunction (Bus, Dev, Func, SsidSvid);
return EFI_SUCCESS;
}
}
}
return EFI_UNSUPPORTED;
}

## Slide 15: Related Files - SetSsidSvidDxe
ProgramSsidSvid ()
  Program a SSID/SVID value to a device (For remaining device).
SetSsidSvidDxe.c
ProgramSsidSvid (
IN EFI_PCI_ROOT_BRIDGE_IO_PROTOCOL *PciRootBridgeIo,
IN UINT8 Bus,
IN UINT8 Dev,
IN UINT8 Func,
IN UINT32 SsidSvid
) {
…
BootScriptPciAddress = S3_BOOT_SCRIPT_LIB_PCI_ADDRESS (Bus, Dev, Func,PCI_SUBSYSTEM_VENDOR_ID_OFFSET);
S3BootScriptSavePciCfgWrite (
S3BootScriptWidthUint32,
BootScriptPciAddress,
1,
&SsidSvid);
...
}

## Slide 16: Customization Steps

## Slide 17: Customization Steps
Step 1: Modify the default PcdDefaultSsidSvid value
  Set the PcdDefaultSsidSvid values in Project.dsc
    gInsydeTokenSpaceGuid.PcdDefaultSsidSvid|XXXXXXXX
Step 2: Modify OemSvcUpdateSsidSvidInfo
  Add the New entry for specific device in SsidTable
  STATIC OEM_SSID_SVID_TABLE SsidTable[] = {
  0xXXXX, DEVICE_ID_DONT_CARE, ProgramSsidSvid0xFFFFXXXX,
  DEVICE_ID_DONT_CARE, DEVICE_ID_DONT_CARE, NULL
  };
  Add the ProgramSsidSvid0xFFFFXXXX function to program the SSID/SVID

## Slide 18: Thanks!