## Slide 1: How to Create New Project
Insyde Software March 2021

## Slide 2: Copyright 2021 Insyde Software Corp., All Rights Reserved.
No part of this publication may be reproduced, transmitted, transcribed, stored in a retrieval system, or translated into any language or computer language, in any form, or by any means, electronic, mechanical, magnetic, optical, chemical, manual or otherwise, without the prior written permission of Insyde Software Corp.
Disclaimer
Insyde Software Corp. (“Insyde”), provides this document and the programs "as is" without warranty of any kind, either expressed or implied, including, but not limited to, the implied warranties of merchantability or fitness for a particular purpose.
This document may contain technical inaccuracies or typographical errors. Changes are periodically made to the information herein; these changes will be incorporated in future revisions of this document. Insyde is under no obligation to notify any person of the changes. Some code names featured in this document are used to identify products that are in development and not yet publicly announced for release. Insyde is not obligated for its accuracy or completeness.
This document may contain third party’s information, features, schedules, code names, and product names, which are based on Insyde’s interpretation available as of the creation of this document and may be changed from time to time. Neither Insyde nor the third party is obligated to notify such change. If you are interested in third party’s information, you may contact the local third party sales office or the local distributor to obtain the latest specifications. All the intellectual property right of any third party information remains to its owner or steward.

## Slide 3: Agenda
Goals & Target Audience
Create New Project
Internal Use

## Slide 4: Goals & Target Audience

## Slide 5: Goals & Target Audience
Target Audience:
  BIOS developers who use InsydeH2O 5.4 (EDK II) to create their firmware products.
Goals:
  Know how to create a new project
Requirements:
  InsydeH2O 5.4 source code

## Slide 6: Create New Project

## Slide 7: Create New Project
Create a new package for your project in $(WORKSPACE)/Board/Intel
(Ex: SamplePkg).
Copy all folders/files from CRB board package (Ex: EagleStreamMultiBoardPkg) to your package.

## Slide 8: Project Package Files
File Name | Description
Makefile | Provides all standard build targets for the Project and any custom build targets.
Project.dsc | Project description file, which lists all Modules to be built, all Library Class mappings and all non-default PCD settings.
Project.env | Symbol definitions shared between Project.dsc and Project.fdf.
Project.fdf | Project flash definition file, which describes how firmware files are put together, combined in firmware volumes and packaged as capsules.
Project.uni | Project-wide strings definition. Strings defined here will override strings defined in individual Modules.
ProjectBuild.bat | Batch file that sets up the build environment for the command line.
ProjectPostBuild.bat | Batch file invoked after the standard build process has completed.
ProjectPreBuild.bat | Batch file invoked before the standard build process has started.
ProjectSetup.bat | Batch file that sets up the build environment.
BuildFsp.cmd | Batch file for building and generating FSP Binary

## Slide 9: Generate The Binary
Dould Click ProjectBuild.bat
  X64: Run “nmake uefi64” or “nmake efidebug”
If building successfully, it will generate the binary in $(WORKSPACE)/Build/$(PROJECT_PKG)/$(BUILD_TARGET)_$(TOOL_CHAIN)/FV/EGLSTRM.fd
Build/EagleStreamMultiBoardPkg/RELEASE_VS2015x86/FV/EGLSTRM.fd
Build/EagleStreamMultiBoardPkg/DEBUG_VS2015x86/FV/EGLSTRM.fd

## Slide 10: Generate The Binary FSP
Dould Click ProjectBuild.bat
  X64 (FSP):
    Run “BuildFsp.cmd /r” or “BuildFsp.cmd /d”
    Run “nmake uefi64fsp” or “nmake efidebugfsp”
If building successfully, it will generate the binary in $(WORKSPACE)/Build/$(PROJECT_PKG)/$(BUILD_TARGET)_$(TOOL_CHAIN)/FV/EGLSTRM.fd
Build/EagleStreamMultiBoardPkg/RELEASE_VS2015x86/FV/EGLSTRM.fd
Build/EagleStreamMultiBoardPkg/DEBUG_VS2015x86/FV/EGLSTRM.fd

## Slide 11: Customize Actions Before or After Creation of the BIOS Binary
KernelPreBuild.bat
  Called by ProjectPreBuild.bat
ChipsetPreBuild.bat
  Commands after calling KernelPreBuild.bat
ProjectPreBuild.bat
  Commands after finishing ChipsetPreBuild.bat
KernelPostBuild.bat
  Called by ProjectPostBuild.bat
ChipsetPostBuild.bat
  Commands after calling KernelPostBuild.bat
ProjectPostBuild.bat
  Commands after finishing ChipsetPreBuild.bat

## Slide 12: Customize Project.dsc
Define the OEM/ODM Project Name
Add/Modify/Remove the specific module/driver/Package
Change Library Class/library instance mapping
Customize PCD values

## Slide 13: Customize Project.fdf
Define FD/FV/Regions for Project
  Name, Size, Base Address, …
Add/Remove Module

## Slide 14: Customize Project.env
Turn on/off the build switches

## Slide 15: Customize Project.uni
Higher priority string definition
#string STR_MISC_BIOS_VERSION #language en-US “BIOS.Version“
#string STR_MISC_SYSTEM_PRODUCT_NAME #language en-US “Product_Name“
#string STR_MISC_BIOS_RELEASE_DATE #language en-US “MM/DD/YYYY“
#string STR_ESRT_FIRMWARE_GUID #language en-US "FFD4675E-FF47-46D9-AC24-8B331F937737"

## Slide 16: Other Customications
Add/Modify/Remove the UEFI driver or Option ROM
Program GPIO setting
LOGO Replacement
…

## Slide 17: Thanks!