## Slide 1: Option ROM
Insyde Software March 2021

## Slide 2: Copyright 2021 Insyde Software Corp., All Rights Reserved.
No part of this publication may be reproduced, transmitted, transcribed, stored in a retrieval system, or translated into any language or computer language, in any form, or by any means, electronic, mechanical, magnetic, optical, chemical, manual or otherwise, without the prior written permission of Insyde Software Corp.
Disclaimer
Insyde Software Corp. (“Insyde”), provides this document and the programs "as is" without warranty of any kind, either expressed or implied, including, but not limited to, the implied warranties of merchantability or fitness for a particular purpose.
This document may contain technical inaccuracies or typographical errors. Changes are periodically made to the information herein; these changes will be incorporated in future revisions of this document. Insyde is under no obligation to notify any person of the changes. Some code names featured in this document are used to identify products that are in development and not yet publicly announced for release. Insyde is not obligated for its accuracy or completeness.
This document may contain third party’s information, features, schedules, code names, and product names, which are based on Insyde’s interpretation available as of the creation of this document and may be changed from time to time. Neither Insyde nor the third party is obligated to notify such change. If you are interested in third party’s information, you may contact the local third party sales office or the local distributor to obtain the latest specifications. All the intellectual property right of any third party information remains to its owner or steward.

## Slide 3: Agenda
Goals & Target Audience
Overview
Related Files
Customization Steps
Internal Use

## Slide 4: Goals & Target Audience

## Slide 5: Goals & Target Audience
Target Audience:
  BIOS developers who use InsydeH2O 5.4 (EDK II) to create their firmware products.
Goals:
  Know how to add / modify an Option ROM in InsydeH2O 5.4.
Requirements:
  InsydeH2O 5.4 source code
  Option ROM binary file

## Slide 6: Overview

## Slide 7: Overview
Option ROMs are add-on code designed to support specific PCI devices.
PCI option ROMs can contain either legacy images or compressed UEFI driver images.
Option ROM images can be included with the PCI device itself, a pointer to which is found in the PCI configuration space, or can be provided by the BIOS.

## Slide 8: Overview
There are three sources of system firmware option ROM images:
  OEM Service OemSvcInstallOptionRomTable
    This function can provide zero or more option ROM images, along with associated Firmware File Name, vendor identifier and device identifier. All option ROMs returned are associated with all boards.
  Auto-generated list of option ROM images
    This list can provide zero or more option ROM images along with associated Firmware File Name, vendor identifier and multiple device identifiers. All option ROMs in this list are associated with all boards.
  Option ROM images listed in the Flash Device Map
    The Flash Device Map can provide zero or more option ROM images along with an image. Each option ROM image can be associated with up to six boards, including the DEFAULT board. Option ROM images can be associated with a vendor identifier and device identifier, or else a bus/device/function number.

## Slide 9: Related Files

## Slide 10: Related Files
Board/Intel/$(PROJECT_PKG)/Library/DxeOemSvcKernelLib/OemSvcInstallOptionRomTable.c
Insyde/InsydeModulePkg/Include/Guid/AutoGenPciOptionRomList.h
Build/$(ProjectPkg)/$(BuidFolder)/FV/ XXXX.FvOpRomList.ffs
Build/$(ProjectPkg)/$(BuidFolder)/FV/ XXXX.FvOpRomList.txt
Insyde/InsydeModulePkg/Universal/CommonPolicy/CommonPciPlatformDxe.c

## Slide 11: OemSvcInstallOptionRomTable.c
Provide OEM to install the PCI Option ROM table and Non-PCI Option ROM table.
OemSvcInstallOptionRomTable.c
OemSvcInstallOptionRomTable (
…
) {
…
switch (RomType) {
case PCI_OPROM:
…
case SYSTEM_ROM:
…
case SYSTEM_OEM_INT_ROM:
…
case SERVICE_ROM:
…
case TPM_ROM:
…
case AMT_ROM:
…
default:
return EFI_SUCCESS;
}
…
return EFI_MEDIA_CHANGED;
}
OemSvcInstallOptionRomTable.c
PCI_OPTION_ROM_TABLE PciOptionRomTable[] = {
{
NULL_ROM_FILE_GUID,
0xffff,
0xffff
}
};
OemSvcInstallOptionRomTable.c
SYSTEM_ROM_TABLE SystemRomTable[] = {
{
// CSM16 binary
SYSTEM_ROM_FILE_GUID,
TRUE,
SYSTEM_ROM
},
{
NULL_ROM_FILE_GUID,
FALSE,
MAX_NUM
}
};

## Slide 12: Auto-generated list of option ROM images
Generate in build time
  The XXXX.FvOpRomList.ffs and XXXX.FvOpRomList.txt will be generate in Build\$(ProjectPkg)\$(BuidFolder)\FV folder.
  XXXX.FvOpRomList.ffs: The table of devices list in binary.
  XXXX.FvOpRomList.txt: This file to explain what device was parsing.
Integrate in runtime
  PCI option rom table will be prepared and used in
  Insyde/InsydeModulePkg/Universal/CommonPolicy/CommonPciPlatformDxe/CommonPciPlatformDxe.c
  Add two new functions:
    CommonPciInstallOptionRomFromOemService (); Higher priority then AutoGen
    CommonPciInstallOptionRomFromAutoGenList ();

## Slide 13: Auto-generated list of option ROM images
Install Option rom to table from OemSvc
CommonPciPlatformDxe.c
CommonPciInstallOptionRomFromOemService (
){
…
Status = OemSvcInstallOptionRomTable (
PCI_OPROM,
(VOID **)&PciOptionRomTable
);
if (Status != EFI_MEDIA_CHANGED) {
return Status;
}
if (PciOptionRomTable == NULL) {
return EFI_NOT_READY;
}
for (TableIndex = 0; PciOptionRomTable[TableIndex].VendorId != 0xFFFF; TableIndex++) {
CommonPciInstallOptionRomTable (PciOptionRomTable + TableIndex);
}
return EFI_SUCCESS;
}

## Slide 14: Auto-generated list of option ROM images
Install Option rom to table from AutoGenList
CommonPciPlatformDxe.c
CommonPciInstallOptionRomFromAutoGenList (
) {
…
Status = GetSectionFromAnyFv (&gAutoGenPciOptionRomListGuid,…);
…
// Check data validation
…
// Put Item
Offset = 0;
Ptr = AutoGenOpRomList;
while (Offset < SectionSize) {
Offset += sizeof (AUTO_GEN_PCI_OPTION_ROM_TABLE) + sizeof (UINT16) * (Ptr->DeviceIdCount - 1);
if (!IsUsbOptionRom (&Ptr->FileName)) {
CopyGuid (&(PciOptionRomTable.FileName), &(Ptr->FileName));
PciOptionRomTable.VendorId = Ptr->VendorId;
for (Index = 0; Index < Ptr->DeviceIdCount; Index++) {
PciOptionRomTable.DeviceId = Ptr->DeviceId[Index];
CommonPciInstallOptionRomTable (&PciOptionRomTable);
}
}
Ptr = (AUTO_GEN_PCI_OPTION_ROM_TABLE *)(((UINTN)AutoGenOpRomList) + Offset);
}
return Status;
}

## Slide 15: Auto-generated list of option ROM images
CommonPciPlatformDxe.c
CommonPciInstallOptionRomTable (
…
){
…
// If find VID and DID is exist, return success.
// Let first install can select option rom from OemSvc.
// The VID and DID is only installed one set.
for (TableIndex = 0; TableIndex < mPciOpRomTableCnt; TableIndex++) {
if ((mPciOpRomTable[TableIndex].VendorId == PciOpRom->VendorId) &&
(mPciOpRomTable[TableIndex].DeviceId == PciOpRom->DeviceId)) {
return EFI_SUCCESS;
}
}
// Check Database size
…
// Put Item
CopyGuid (&(mPciOpRomTable[mPciOpRomTableCnt].FileName), &(PciOpRom->FileName));
mPciOpRomTable[mPciOpRomTableCnt].VendorId = PciOpRom->VendorId;
mPciOpRomTable[mPciOpRomTableCnt].DeviceId = PciOpRom->DeviceId;
mPciOpRomTableCnt++;
return EFI_SUCCESS;
}

## Slide 16: CommonPciPlatformDxe.c
The GetPciRom() function provides or substitutes the option ROM image for the device.
CommonPciPlatformDxe.c
CommonGetPciRom (
…
){
// Get Segment, Bus, Device, Function, Vendor ID and Device ID
…
DxeCsSvcSkipGetPciRom (Segment, Bus, Device, Function, VendorId, DeviceId, &SkipGetPciRom);
…
Status = OemSvcSkipLoadPciOptionRom (Segment,Bus,Device,Function, VendorId, DeviceId, &SkipGetPciRom);
if ((Status == EFI_SUCCESS) || (Status == EFI_MEDIA_CHANGED)) {
Status = EFI_NOT_FOUND;
…
} else {
// Get PCI Option ROM from FV
Status = GetFromFv (VendorId, DeviceId, RomImage, RomSize);
…
}
…
return Status;
}

## Slide 17: Customization Steps

## Slide 18: Customization Steps
UEFI Driver Binary
  Step 1: Create new folder for UEFI Driver Binary
    UEFI Driver binary file
    Ex: Board/Intel/$(PROJECT_PKG)/Binary/SampleRom/SampleRom.efi
  Step 2: Add it to Project.dsc and Project.fdf
    Remember to disable the one if it is imported by other package

## Slide 19: Customization Steps
Legacy Option ROM
  Step 1: Create new folder for Legacy Option ROM
    UEFI Driver binary file
    Ex: Board/Intel/$(PROJECT_PKG)/Binary/SampleRom/SampleRom.bin
  Step 2: Add it to Project.fdf
    Remember to disable the one if it is imported by other package
  Step 3: Add GUID definition to OemSvcInstallOptionRomTable.c
  Step 4: Add Option ROM data to PciOptionRomTable in OemSvcInstallOptionRomTable.c

## Slide 20: Thanks!