## Slide 1: Microcode
Insyde Software July 2022

## Slide 2: Copyright 2022 Insyde Software Corp., All Rights Reserved.
No part of this publication may be reproduced, transmitted, transcribed, stored in a retrieval system, or translated into any language or computer language, in any form, or by any means, electronic, mechanical, magnetic, optical, chemical, manual or otherwise, without the prior written permission of Insyde Software Corp.
Disclaimer
Insyde Software Corp. (“Insyde”), provides this document and the programs "as is" without warranty of any kind, either expressed or implied, including, but not limited to, the implied warranties of merchantability or fitness for a particular purpose.
This document may contain technical inaccuracies or typographical errors. Changes are periodically made to the information herein; these changes will be incorporated in future revisions of this document. Insyde is under no obligation to notify any person of the changes. Some code names featured in this document are used to identify products that are in development and not yet publicly announced for release. Insyde is not obligated for its accuracy or completeness.
This document may contain third party’s information, features, schedules, code names, and product names, which are based on Insyde’s interpretation available as of the creation of this document and may be changed from time to time. Neither Insyde nor the third party is obligated to notify such change. If you are interested in third party’s information, you may contact the local third party sales office or the local distributor to obtain the latest specifications. All the intellectual property right of any third party information remains to its owner or steward.

## Slide 3: Agenda
Goals & Target Audience
Boot Flow
Related Files
Customization Steps
Internal Use

## Slide 4: Goals & Target Audience

## Slide 5: Goals & Target Audience
Target Audience:
  BIOS developers who use InsydeH2O 5.4 (EDK II) to create their firmware products.
Goals:
  Understand how to change the CPU Microcode for project requirement.
  Understand the Microcode update stage during the POST.
Requirements:
  InsydeH2O 5.4 source code
  Microcode released from Intel

## Slide 6: Boot Flow

## Slide 7: Boot Flow
EFI Driver Dispatcher
Security (SEC)
Power On
Shutdown
[..Platform Initialization..]
[..OS Boot..]
Pre EFI Initialization
(PEI)
Driver Execution Environment (DXE)
Boot Dev Select (BDS)
UEFI & OS Loader Handshake
Runtime (RT)
Pre Verifier
Architectural Protocols
Final OS Boot Loader
Final OS Environment
CPU Init
Chipset Init
Board Init
PEI Core
OS-Present App
OS-Absent App
Transient OS Environment
Transient OS Boot Loader
Device, Bus, or Service Driver
Boot Manager
Verify
EFI/UEFI Interfaces
ProcessorStartup.nasm

## Slide 8: Related Files

## Slide 9: Related Files
Intel/EagleStream/($CHIPSET_PKG)/Package.dsc
Intel/EagleStream/($CHIPSET_PKG)/Binary/Microcode
  Microcode1.inf
  Microcode2.inf
  *.INC
Board/Intel/$(PROJECT_PKG)/FlashRegionDefines.fdf
Board/Intel/$(PROJECT_PKG)/Project.fdf
Intel/EagleStream/ServerSiliconPkg/Library/ProcessorStartup/Ia32/ProcessorStartupSpr.nasm

## Slide 10: Related Files
Intel/EagleStream/$(CHIPSET_PKG)/Package.dsc
  [Components.$(DXE_ARCH)]
  $(CHIPSET_PKG)/Binary/Microcode/Microcode1.inf
  $(CHIPSET_PKG)/Binary/Microcode/Microcode2.inf
Intel/EagleStream/$(CHIPSET_PKG)/Binary/Microcode
  Microcode#.inf
  *.INC
    Put the microcode (*.INC) into the folder
    .
    [Defines]
    INF_VERSION = 0x00010005
    BASE_NAME = Microcode2
    FILE_GUID = B53105F3-3B4E-41FB-8310-108F64F0E297
    MODULE_TYPE = USER_DEFINED
    VERSION_STRING = 1.0
    [Sources]
    m_10_806f4_830002a0.inc
    [Defines]
    INF_VERSION = 0x00010005
    BASE_NAME = Microcode1
    FILE_GUID = 197DB236-F856-4924-90F8-CDF12FB875F3
    MODULE_TYPE = USER_DEFINED
    VERSION_STRING = 1.0
    [Sources]
    m_87_806f3_8d000510.inc

## Slide 11: Related Files
Board/Intel/$(PROJECT_PKG)/FlashRegionDefines.fdf
DEFINE FLASH_REGION_NV_COMMON_STORE_SUBREGION_MICROCODE_OFFSET = $(FLASH_REGION_INSYDE_BOOT_LOGO_OFFSET) + $(FLASH_REGION_INSYDE_BOOT_LOGO_SIZE)
DEFINE FLASH_REGION_NV_COMMON_STORE_SUBREGION_MICROCODE2_OFFSET = $(FLASH_REGION_NV_COMMON_STORE_SUBREGION_MICROCODE_OFFSET) + $(FLASH_REGION_NV_COMMON_STORE_SUBREGION_MICROCODE_SIZE)
DEFINE FLASH_REGION_NV_COMMON_STORE_SUBREGION_MICROCODE_SIZE = 0x00180000
DEFINE FLASH_REGION_NV_COMMON_STORE_SUBREGION_MICROCODE2_SIZE = 0x00180000

## Slide 12: Related Files
Board/Intel/$(PROJECT_PKG)/Project.fdf
$(FLASH_REGION_NV_COMMON_STORE_SUBREGION_MICROCODE_OFFSET)|$(FLASH_REGION_NV_COMMON_STORE_SUBREGION_MICROCODE_SIZE)
gInsydeTokenSpaceGuid.PcdFlashNvStorageMicrocodeBase|gInsydeTokenSpaceGuid.PcdFlashNvStorageMicrocodeSize
RegionType = gH2OFlashMapRegionMicrocodeGuid
FILE = $(OUTPUT_DIRECTORY)/$(TARGET)_$(TOOL_CHAIN_TAG)/X64/Microcode1.bin
$(FLASH_REGION_NV_COMMON_STORE_SUBREGION_MICROCODE2_OFFSET)|$(FLASH_REGION_NV_COMMON_STORE_SUBREGION_MICROCODE2_SIZE)
gCpuUncoreTokenSpaceGuid.PcdFlashNvStorageMicrocode2Base|gCpuUncoreTokenSpaceGuid.PcdFlashNvStorageMicrocode2Size
RegionType = gH2OFlashMapRegionMicrocodeGuid | 0x1
FILE = $(OUTPUT_DIRECTORY)/$(TARGET)_$(TOOL_CHAIN_TAG)/X64/Microcode2.bin

## Slide 13: Related Files
Intel/EagleStream/ServerSiliconPkg/Library/ProcessorStartup/Ia32/ ProcessorStartupSpr.nasm
ProcessorStartupSpr.nasm
global ASM_PFX(ProcessorStartup)
ASM_PFX(ProcessorStartup):
…
PORT80 (MICROCODE_POST_CODE)
…
CALL_MMX3 ASM_PFX(LoadProcessorMicrocode)
…
ProcessorStartupCore.nasm
global ASM_PFX(LoadProcessorMicrocode)
ASM_PFX(LoadProcessorMicrocode):
CALL_MMX4 ASM_PFX(OemFindMicrocode)
…
ProcessorStartupOem.nasm
global ASM_PFX(OemFindMicrocode)
ASM_PFX(OemFindMicrocode):
mov esi, [ASM_PFX(PcdGet32 (PcdFlashNvStorageMicrocodeBase))]
…
; Check for valid microcode header
…
; Check if signature and platform ID match
…
; Check if extended header exists
; First check if total_size and data_size are valid
…
; Get count of extended structures
…
; Check if extended signature and platform ID match
…
; Check if any more extended signatures exist
…
; Verify this microcode update is not already loaded
…

## Slide 14: Customization Steps

## Slide 15: Customization Steps
Step 1: Decide how much ROM space you want to reserve for Microcode.
  Board/Intel/$(PROJECT_PKG)/FlashRegionDefines.fdf
Step 2: Decide which microcode you want to put into the firmware.
  Intel/EagleStream/$(CHIPSET_PKG)/Binary/Microcode/Microcode#.inf
  Put the microcode (*.INC) into the folder

## Slide 16: Customization Steps
If you want to put the Microcode into another place.
Declare using your Microcode module instead of original one.
Board/Intel/$(PROJECT_PKG)/Project.dsc
  [Components.$(DXE_ARCH)]
  …
  !disable $(CHIPSET_PKG)/Binary/Microcode/Microcode#.inf
  $(PROJECT_PKG)/Binary/Microcode/MicrocodeUpdates.inf
  …

## Slide 17: Thanks!